## Slide 1: TIA Portal LXM32M – PROFINET –
Example Program for S7-1200/1500
using “Lexium32 PLCopen library”

## Slide 2: Example LXM32 TIA S7-1200/1500 Overview
Project file for Siemens TIA Portal V13:
PLCopen_Example_LXM32_S7_1200_1500
LXM32M Profibus PLCopen Library file for Siemens TIA Portal V13: SE_Motion_LXM32_1200_1500_V1001.zal13
Manual for PLCopen Library
Documentation PLCopen Library for LXM32_S7_1200_1500_V1001_EN.pdf

## Slide 3: Example LXM32 TIA S7-1200/1500 Communication settings LXM32M
No explicite address setting on Lexium 32M is needed, if the configuration
tool of the IO controller is used.
The PROFINET interface is factory-set to DCP (Discovery Configuration
Protocol). This setting does not have to be changed.
 After „Factory setting“ on Lexium 32M, the drive is ready prepared for the PROFINET –communication with the Siemens CPU 1200/1500.

## Slide 4: Example LXM32 TIA S7-1200/1500 GSD (Generic Station Description)
- Install GSD File in TIA Portal
TIA Portal -> Options -> Manage general station description files (GSD) - Select Source path -> Select file -> Installstall

## Slide 5: Example LXM32 TIA S7-1200/1500 TIA – Device configuration
Adding a CPU and Lexium32 drive
and link the PN connection from CPU to Lexium 32

## Slide 6: Example LXM32 TIA S7-1200/1500 TIA – Device configuration
Device name setting

## Slide 7: Example LXM32 TIA S7-1200/1500 TIA – Device configuration
Assign Device name

## Slide 8: Example LXM32 TIA S7-1200/1500 TIA – Device configuration
The Hardware Indentifier of the “DriveProfileLexium1” is needed when Init_LXM32_1200_1500 is called in OB100

## Slide 9: Example LXM32 TIA S7-1200/1500 OB1 – Main Program
Call of PLCopen function blocks Drive 1
Example sequence

## Slide 10: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
Example_Sequence_LXM32 (FB3) starts automatically with the input variable “ExampleSequence.ix_start”. It will be set to ´TRUE´ in Startup OB (OB100).
State 0: Wait for “Start” Reset all execute commands.
State 1: Fault reset on (MC_Reset)
Enable „MC_Read_Status“ and „MC_Read_Axis_Error“
State 2: Wait for Drive “Ready to switch on” (Status 4)
State 3 and 4: Write Scaling factor to 10000 USR units.
State 5: Deactivate Limit switch „LIMP“
State 6: Deactivate Limit switch „LIMN“
State 7: Enable power stage (MC_Power)
State 8: Reference movement - Homing Type 33 (MC_Home)
State 9: Move absolute to 100000 (MC_MoveAbsolute)
State 10: Move absolute to 0 (MC_MoveAbsolute)
State 11: Move relative to 200000 (MC_MoveRelative)
and jump back to state 9
State 100: Error State – reading ErrorID
and wait for reset input „ixErrorReset“
State 101: Check for MC_Reset.Done

## Slide 11: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 0: Wait for “Start” -> Reset all execute commands.

## Slide 12: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 1: - Fault reset (MC_Reset)
- Enable „MC_Read_Status“ and „MC_Read_Axis_Error“

## Slide 13: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 2: Wait for Drive “Ready to switch on” (Status 4)

## Slide 14: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 3 and 4: Write Scaling factor to 10000 USR units

## Slide 15: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 5: Deactivate Limit switch „LIMP“

## Slide 16: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 6: Deactivate Limit switch „LIMN“

## Slide 17: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 7: Enable power stage (MC_Power)

## Slide 18: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 8: Reference movement to Index pulse (MC_Home)

## Slide 19: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 9: Move absolute to 100000 (MC_MoveAbsolute)

## Slide 20: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 10: Move absolute to 0 (MC_MoveAbsolute)

## Slide 21: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 11: Move relative to 200000 (MC_MoveRelative)
and jump back to state 9

## Slide 22: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 100: Read LXM32 ErrorID and wait for “ixErrorReset”

## Slide 23: Example LXM32 TIA S7-1200/1500 Example_Sequence_LXM32(FB3)
State 101: Check for MC_Reset.Done